## Slide 1
NUCLEAR MEDICINE
IMAGING SYSTEMS

## Slide 2
Humans does not have a sense with which he could register ionizing radiation
It can only be registered with specially designed DETECTOR devices
Ionizing Detectors

## Slide 3
Ionizing Detectors
1
What are Ionizing Detectors?
Ionizing detectors are devices that detect ionizing radiation such as alpha and beta particles, gamma rays, and X-rays. They work on the principle of ionization which occurs when radiation interacts with the detector material.
2
Types of Ionizing Detectors
There are several types of ionizing detectors including Geiger-Muller tubes, proportional counters, and semiconductor detectors. Each type has its own working principle, advantages, and disadvantages.
3
Applications of Ionizing Detectors
Ionizing detectors have a wide range of applications such as in medical imaging. They are also used for detecting radiation in the environment and in food.

## Slide 4
Types of ionizing detectors
Based on the medium i which ionization occurs
Gass filled detectors
Liquid Detectors
Solid state

## Slide 5: Gass filled detectors
A vacuumed cylindrical tube with a positive electrode along the axis of the cylinder. The pipe wall is at negative voltage and is grounded. The tube is filled with a working gas (most often a mixture of argon, neon and helium) and a substance that serves for extinguishing (quenching), i.e. preventing the formation of a Volta arc in the tube (most often it is ethyl alcohol)

## Slide 6: Gass filled detectors

## Slide 7
Geiger Counter
The classic gas-filled detector that measures the ionizing particles in the air.
Proportional Counter
Higher level of accuracy and precision than Geiger counters. Measures the energy deposited by particles, not just their number.
Ion Chambers
Used for measuring radiation levels in air, water, or other materials.
GM Tube
Measures radiation by detecting ion pairs formed in the gas filled tube.
Gass filled detectors

## Slide 8
Geiger-Müller counter
Radiation monitoring

## Slide 9
Working Principles of the Geiger-Müller Counter
1
Gas Filled Tube
The Geiger-Müller counter measures ionizing radiation through the use of a gas-filled tube.
2
Gamma Ray Detection
When gamma rays penetrate the walls of the gas tube, they ionize argon gas atoms and produce ions and electrons.
3
Amplification
These charged particles are then amplified through several stages of electronic amplification, and produce a measurable electrical pulse.
4
Counting Mechanism
Finally, the electrical pulse is counted, and hazardous levels of ionizing radiation are determined.

## Slide 10
Advantages and Disadvantages
of the Geiger-Müller Counter
Advantages
Disadvantages
Ease of use
Saturates at high radiation levels
Low cost
Cannot differentiate between types of radiation
High accuracy
Accuracy declines with higher radiation levels
Fast response time
Requires calibration over time

## Slide 11
Liquid Detectors
Working Principle
Liquid detectors use a liquid scintillator or other liquid materials to detect radiation. When radiation interacts with the liquid, it produces scintillations or flashes of light, which can be detected and measured.
Components
Liquid detectors consist of a scintillator material, a photomultiplier tube to detect the scintillations, and electronics to amplify and process the signal.
Advantages and Disadvantages
Liquid detectors have high sensitivity, good energy resolution, and can be used in a variety of applications such as in medical imaging and particle physics experiments. However, they may be costly, require careful handling, and produce radioactive waste.

## Slide 12
Scintillation Detectors
1
Principle
Converts ionizing radiation into flashes of light, which are then measured and counted.
This interaction generates light in the ultraviolet to visible range.
Scintillators capture this light and convert it into an electrical signal that can be measured and analyzed
2
Types
There are organic and inorganic scintillators, each with its own properties and applications
3
Examples
Sodium Iodide, Bismuth Germanate, Anthracene, NaI (Tl) Scintillation Detector
.
.
Organic scintillators are made of complex molecules containing aromatic compounds that produce light when excited.

## Slide 13
Pros and Cons of Scintillation Detectors
Pro: High Efficiency
Scintillation detectors can achieve high detection efficiencies for a wide range of radiation energies and types.
Pro: Fast Response Time
Scintillation detectors have a fast response time and can capture the timing information of radiation events with excellent precision.
Con: Temperature Sensitivity
Scintillators can be sensitive to temperature changes that affect their output, requiring careful calibration and operation.
Con: Radiation Damage
Scintillators can be damaged by the same radiation they are meant to detect, limiting their lifetime and sensitivity under high doses.

## Slide 14
It consists of a scintillator which generates photons in response to incident radiation, a sensitive photodetector (usually a photomultiplier tube (PMT), a charge-coupled device (CCD) camera, or a photodiode), which converts the light to an electrical signal and electronics to process this signal.
NaI (Tl) crystal
PMT
Scintillation Detectors

## Slide 15
Solid-State Detectors
Properties
Uses a solid material such as silicon or germanium crystal
Converts charged particles into electronic signals
Applications
Used in medical imaging such as PET and CT scans
Image of Solid-State Detector
High sensitivity and spatial resolution
Excellent imaging
Silicon, Cadmium Zinc Telluride (CZT), Germanium, Diamond, and Sapphire detectors.

## Slide 16
Comparison with Other Radiation Detectors
Scintillation Detector
A scintillation detector detects ionizing radiation by using crystal materials.
Ionization Chamber
An Ionization chamber detects and measures ionizing radiation by using an ion chamber filled with gas.
Proportional Counter
A proportional counter detects particles of ionizing radiation and measures their energy levels, such as in mass spectrometry.

## Slide 17
Conclusion
Detector Type
Advantages
Disadvantages
Ionizing
High sensitivity and can be used in a variety of applications
May require high voltage power supplies and may be sensitive to temperature and pressure changes
Gas-filled
High sensitivity, good energy resolution, and can be used in high radiation environments
Requires high voltage power supplies and may be sensitive to temperature and pressure changes
Liquid
High sensitivity and good energy resolution
May be costly, require careful handling, and produce radioactive waste
Solid-state
High sensitivity and spatial resolution
May be costly and require specialized handling and processing
Scintillation
High sensitivity and good energy resolution
May require careful handling and processing

## Slide 18
Medical Imaging devices

## Slide 19
X-rays
X-rays are a type of electromagnetic radiation that are used to create images of the inside of the body.

## Slide 20: MDCT Imaging
A.M. Cormac, Sir G.N.Hounsfield 1979
MDCT imaging is a type of computed tomography that uses multiple detectors to capture cross-sectional images of the body.
MDCT images are produced by rotating an x-ray tube around the body and using multiple detectors to measure the resulting x-rays. The images are then reconstructed using computer software.

## Slide 21
Linear Accelerator (LINAC)
LINAC, Y knife, X knife
Linear accelerators are used to deliver high-energy radiation to cancerous tissue while sparing surrounding healthy tissue. The machines use electricity to accelerate electrons to near-light speeds, which creates high-energy photons that can penetrate tissue.
LINACs are used for external beam radiation therapy to treat cancerous tumors throughout the body, including the lung, prostate, breast, and head and neck.

## Slide 23
Gamma Camera Imaging

## Slide 24
Principles of Operation
1
Gamma Ray Detection
The camera detects gamma rays emitted from the patient's body after being administered with a radioactive tracer. These rays are typically in the 100 keV to 2 MeV range.
2
Scintillation Detection
The detector converts gamma rays into visible light, which is captured by the camera to form an image of the organ or tissue being studied.
3
Image Reconstruction
The camera uses sophisticated algorithms to convert the detected light into a high resolution 2D or 3D image. This information is then analyzed by physicians to make a diagnosis or determine treatment options.

## Slide 25
Gamma Camera Components
Detector Head
scintillator: single photoluminescent crystal, usually made from thallium-activated sodium iodide. it detects gamma rays emitted by the patient and converts them into an electrical signal.
photomultiplier tubes
preamplifiers
electronics including: analog to digital converters, digital summing and positioning circuits and correction circuits

## Slide 26
Parallel hole
Pinhole Fan beam (diverging)
Cone beam (converging)
The collimator is a lead shield with small holes that direct gamma rays towards the detector head. It helps to improve image quality and reduce background radiation noise.
Collimator

## Slide 27
Control Computer
Advantages
Image reconstruction
Storage
Telemedicine
The computer controls the movement of the detector head and processes the imaging data. It allows physicians to view, manipulate, and analyze the images captured by the camera.

## Slide 29
Advantages and Limitations
Advantages
Safe, painless, and non-invasive
Allows physicians to view internal organs and tissues in real time
Can detect problems at a cellular level
Limitations
Expensive, clinical centers
Can expose patients to a small amount of radiation
Requires trained technicians to operate and interpret results

## Slide 30
SCINTIGRAPHY
NUCLEAR MEDICINE IMAGING
Scintigraphy (from Latin scintilla, "spark"), also known as a gamma scan, is a diagnostic test in nuclear medicine, where radioisotopes attached to drugs that travel to a specific organ or tissue (radiopharmaceuticals) are taken internally and the emitted gamma radiation is captured by external detectors (gamma cameras) to form two-dimensional images
In contrast, SPECT form 3-dimensional images and are therefore classified as separate techniques from scintigraphy, although they also use gamma cameras to detect internal radiation

## Slide 31
SCINTIGRAPHY
NUCLEAR MEDICINE IMAGING
Scintigraphy is a molecular imaging technique that involves the use of radioisotopes to generate images of a patient's internal organs and tissues.
Scintigraphy is a safe and non-invasive diagnostic tool that can provide accurate and detailed images of the body's internal structures and functions.
Functional Imaging
Track metabolic processes and biochemical activities in real-time without invasive procedures.

## Slide 32
Radiopharmaceuticals
Composition
Radiopharmaceuticals contain radioactive material and biologically active molecules that selectively adhere to specific disease sites in the body.
Preparation
These substances are carefully prepared and quality-tested in labs to ensure that they are both safe and effective for clinical use.
Injection
A radiopharmaceutical is injected into the patient's bloodstream, where it will travel to the intended organ or tissue being studied.

## Slide 33
Advantages of Scintigraphy
Increased Sensitivity
Scintigraphy can detect abnormalities much earlier than traditional imaging methods, allowing for earlier diagnosis and better outcomes.
Non-Invasive
Unlike other diagnostic methods, scintigraphy does not require surgical or invasive procedures, reducing risks and ensuring a less painful and safer diagnosis experience.
Functional and Anatomical imaging in one
Scintigraphy produces a high-resolution anatomical image combined with a functional image that displays metabolic activities effectively.

## Slide 34
Types of Imaging
Single-Photon Emission Computed Tomography (SPECT)
SPECT uses a rotating gamma camera to acquire images from different angles. It is used to study the function and structure of organs such as the brain, heart, and liver.
Positron Emission Tomography (PET)
PET uses a gamma camera to detect positron emissions from the patient's body. It is used to study metabolic functions and diagnose cancer, dementia, and other diseases.
Planar Scintigraphy
Planar scintigraphy captures 2D images of a patient. It is commonly used to study bone disorders and lung function.
Hybrid Scanners
Hybrid scanners combine SPECT or PET with a CT scanner, providing both structural and functional information about the body.

## Slide 35
Negative scan
Planar Scintigraphy
131I
Positive scan
131I-MIBG
99mTc-Tektrotyd

## Slide 36
Generation of 2D planar projections by rotating the detector around the axis of rotation (of the patient) or in some other combination depending on the construction of the camera and the type of study being performed.
SINGLE PHOTON EMISSION COMPUTED TOMOGRAPHY (SPECT)

## Slide 37
Nuclear medicine imaging

## Slide 38
“eZ-Scope-handheld”
Nuclear medicine imaging

## Slide 39
Positron emission tomography (PET)
11C 13N 15O 18F
Annihilation photons are emitted approximately at an angle of 180° and are registered by the so-called detector rings. Thus, all the data are obtained simultaneously (cross sections), which later participate in the 3D reconstruction of the image.
PET scans detect gamma rays emitted indirectly by a positron-emitting tracer injected into the body.

## Slide 40: Hybrid imaging
Prvi PET/CT hibridni sistem
Morfofunkcionalni imidžing
2007
Prvi PET/MRI hibridni sistem
2010
Prvi time-of-flight WB PET-MRI
Morfofunkcionalni imidžing
Prvi BGO
PET skener
Metabolički imidžing
1978
2003
Prvi SPECT/CT hibridni sistem
Morfofunkcionalni imidžing
1998
Prvi All-in-one SPECT/PET/CT/MRI
Lu1.8Gd0.2SiO5 (Ce) detektor
2013
Morfofunkcionalni imidžing

## Slide 41
Hybrid imaging: SPECT-PET/CT
SPECT/PET + CT > SPECT/PET i CT
combines the functional and molecular information from PET scans with the anatomical information from CT scans to provide detailed images of the body.
have higher accuracy than either PET or CT scans alone; early detection with unprecedented details; and new therapies for cancer and other chronic diseases.
offer increased accuracy in diagnosing cancer, tracking treatment progress, and planning radiation therapy. It can also help detect heart disease and neurological disorders.

## Slide 42
SPECT
CT
SPECT
CT
Hybrid imaging: SPECT-PET/CT

## Slide 43
SPECT
CT
SPECT
CT
Hybrid imaging: SPECT-PET/CT

## Slide 44
Hybrid imaging: SPECT-PET/CT

## Slide 45
SPECT
Finctional imaging SPECT/PET
CT
+
Anatomic imaging CT
Hybrid imaging: SPECT-PET/CT

## Slide 46
  Precise anatomical localization of functional changes (planar/SPECT/PET)
  Increased sensitivity
  Increasing specificity
  Improvement of attenuation correction
  ↓
  Early detection and monitoring of changes Therapy planning
  Therapy monitoring
Hybrid imaging: SPECT-PET/CT
Notes: Modified Slide

## Slide 47
Hybrid imaging: SPECT-PET/CT

## Slide 48
Hybrid imaging: SPECT-PET/MRI

## Slide 49
Hybrid imaging: SPECT-PET/MRI

## Slide 51
From anatomy to molecular imaging Imaging biological parameters
Anatomy
Biology
MRS
NM/PET
MRI
X-Ray Angio
Echo, NM/PET
X-Ray
MSCT
Optical
Metabolism
Receptors
Pump function
Perfusion
Gene expression
Signal transduction
Stem cell function
Nanosystems
Protein dynam.
Zeptomolar 10-21 Mole/L
Femtomolar 10-15 Mole/L
Picomolar 10-12 Mole/L
Micromolar 10-6 Mole/L
Millimolar 10-3 Mole/L
Nanomolar 10-9 Mole/L
Attomolar 10-18 Mole/L

## Slide 52
THANKS FOR YOUR ATTENTION