## Slide 1: IMAGING PROCEDURES IN ONCOLOGY: RADIOLOGICAL DIAGNOSIS Prof. dr Radiša Vojinović
University of Kragujevac
Faculty of Medical Sciences
Department of Radiology

## Slide 2: Medical imaging
Medical imaging is the technique and process of imaging the interior of a body for clinical analysis and medical intervention, as well as visual representation of the function of some organs or tissues (physiology)
Medical imaging seeks to reveal internal structures hidden by the skin and bones, as well as to diagnose and treat disease
Medical imaging also establishes a database of normal anatomy and physiology to make it possible to identify abnormalities
Although imaging of removed organs and tissues can be performed for medical reasons, such procedures are usually considered part of pathology instead of medical imaging

## Slide 3: Medical imaging
Medical imaging is often perceived to designate the set of techniques that noninvasively produce images of the internal aspect of the body
In this restricted sense, medical imaging can be seen as the solution to mathematical inverse problems
This means that cause (the properties of living tissue) is inferred from effect (the observed signal)
In the case of medical ultrasound, the probe consists of ultrasonic pressure waves and echoes that go inside the tissue to show the internal structure
In the case of projectional radiography, or computed tomography (CT), the tube uses X-ray radiation, which is absorbed at different rates by different tissue types such as bone, muscle, and fat

## Slide 4: Medical imaging
Devices that perform medical imaging
  Radiography (projection radiography and fluoroscopy)
  Ultrasound
  Computed tomography
  Magnetic resonance imaging
  Gamma cameras
  PET
  SPECT

## Slide 5: X-ray: what is this?
X-rays are a form of electromagnetic energy formed when high-speed electrons bombard a tungsten anode target
Like light energy, these useful rays have properties of waves and particles
However, X-rays have a much shorter wavelength than visible light, allowing tham to penetrate matter
Most X-rays have a wavelength ranging from 10 nanometers to 10 picometers

## Slide 6: A historical view of x-rays
In many languages, X-radiation is referred to as Röntgen radiation, after the German scientist Wilhelm Conrad Röntgen, who discovered it on November 8, 1895.
He named it X-radiation to signify an unknown type of radiation
Röntgen received the first Nobel Prize in Physics for his discovery

## Slide 7: A historical view of x-rays
The first tube with which Roentgen discovered X-rays
Hand mit Ringen (Hand with Rings): print of Wilhelm
Röntgen's first "medical" X-ray, of his wife's hand

## Slide 8: X-ray tube
An X-ray tube is a vacuum tube that converts electrical input power into X-rays
The availability of this controllable source of X-rays created the field of radiography, the imaging of partly opaque objects with penetrating radiation
In contrast to other sources of ionizing
radiation, X-rays are only produced as
long as the X-ray tube is energized

## Slide 9: X-ray machine for radiography
Projectional radiography, also known as conventional radiography, is a form of radiography and medical imaging that produces two-dimensional images by X-ray radiation
The image acquisition is generally performed by radiographers, and the images are often examined by radiologists
Both the procedure and any resultant images are often simply called 'X-ray'

## Slide 10: X-ray machine for radiography
Plain radiography or roentgenography generally refers to projectional radiography (without the use of more advanced techniques such as computed tomography that can generate 3D-images)
Plain radiography can also refer to radiography without a radiocontrast agent or radiography that generates single static images, as contrasted to fluoroscopy, which are technically also projectional

## Slide 11: Basics of X-ray images, conical projection
The definition of an X-ray image is:
  X-ray image represents a conical projection of the body in one plane, whichit is created by the summation of the projection of all layers of the body through which the x-rays pass

## Slide 12: Physiological contrasts on radiography
The five basic radiographic densities:
  Metal (Bright white)
  Mineral (White)
  Fluid/soft tissue (Gray)
  Fat (Dark gray)
  Air (Black)

## Slide 13: Types of X-ray machines
Classic X-ray machine for radiographs

## Slide 14: Types of X-ray machines
Interventional X-ray machine

## Slide 15: ULTRASONOGRAPHY (US)

## Slide 16: Physical principles of ultrasound
Ultrasound is sound with frequencies greater than 20 kilohertz
This frequency is the approximate upper audible limit of human hearing in healthy young adults
The physical principles of acoustic waves apply to any frequency range, including ultrasound
Ultrasonic devices operate with frequencies from 2 MHz up to 30 Megahertz

## Slide 17: Ultrasound
Medical ultrasound is an ultrasound-based diagnostic medical imaging technique used to visualize muscles, tendons, and many internal organs to capture their size, structure and any pathological lesions with real time tomographic images
Ultrasound has been used by radiologists and sonographers to image the human body for at least 70 years and has become a widely used diagnostic tool
The technology is relatively inexpensive and portable, especially when compared with other techniques, such as magnetic resonance imaging (MRI) and computed tomography (CT)

## Slide 18: Ultrasound
Ultrasound is also used to visualize fetuses during routine and emergency prenatal care
As currently applied in the medical field, properly performed ultrasound poses no known risks to the patient
Sonography does not use ionizing radiation, and the power levels used for imaging are too low to cause adverse heating or pressure effects in tissue
Although the long-term effects due to ultrasound exposure at diagnostic intensity are still unknown, currently most doctors feel that the benefits to patients outweigh the risks

## Slide 19: Properties of ultrasonic waves
Ultrasonic waves have two essential properties: speed and frequency
They have smaller wavelengths
As a result, their penetrating power is high
The relationship between speed, frequency and wavelength is as follows:
  speed = frequency x wavelengths
Ultrasonic waves cannot travel through vacuum (the x-ray propagates through the vacuum)

## Slide 20: Properties of ultrasonic waves
Ultrasonic waves travel at the speed of sound in the medium
The speed of ultrasonic waves depends on the density of the medium
They have maximum velocity in a denser medium
In a homogeneous medium, ultrasonic waves travel at a constant velocity
In low viscosity liquids, ultrasonic waves produce vibrations

## Slide 21: Properties of ultrasonic waves
The higher frequency and shorter wavelength of ultrasound waves results in better spatial resolution
Increasing the frequency affects:
  increase in resolution - better visibility of smaller objects
  reduction of penetration - lower penetration depth
  better directivity (collimation) of waves
Lower frequency → greater penetration (examination of deeper tissues)
Higher frequency → less penetration but better differentiation of details (examination of superficial organs)

## Slide 22: Properties of ultrasonic waves - attenuation
Attenuation is the process of weakening ultrasound waves
Ultrasound waves undergo reflection, refraction, dispersion and absorption
Reflection

## Slide 23: Properties of ultrasonic waves - attenuation
dispersion refraction

## Slide 24: Properties of ultrasonic waves - attenuation
Absorption represents the conversion of a part of the energy of ultrasound waves into heat

## Slide 25: Ultrasound
right kidney liver cancer

## Slide 26: Ultrasound
pancreatic cancer bladder

## Slide 27: Ultrasound transducer
An ultrasound transducer converts electrical energy into mechanical (sound) energy and back again, based on the piezoelectric effect
It is the hand-held part of the ultrasound machine that is responsible for the production and detection of ultrasound waves

## Slide 28: Ultrasound
Ultrasound waves are produced by a transducer, which can both emit ultrasound waves, as well as detect the ultrasound echoes reflected back
In most cases, the active elements in ultrasound transducers are made of special ceramic crystal materials called piezoelectrics
These materials are able to produce sound waves when an electric field is applied to them, but can also work in reverse, producing an electric field when a sound wave hits them

## Slide 29: COMPUTED TOMOGRAPHY (CT)

## Slide 30: History of CT
Half a century has passed since the discovery of computerized tomography (CT-Computerized Tomography), the greatest advance in diagnostic radiology after Roentgen's discovery of X-rays at the end of the 19th century
It is based on X-ray radiation, and is a radiological diagnostic modality that involves computer reconstruction of the cross-section of the body based on multiple measurements of the degree of attenuation (weakening) of directed X-rays
Another essential component of CT is tomography, which requires a mathematical procedure for image processing with the help of computers and software in them

## Slide 31: History of CT
The cross-sections that are obtained as a result of the examination are a computer-processed projection of part of the patient's body, which can be processed in various ways with further software procedures, so reconstructions in other planes are also obtained
Credit for the discovery of CT goes to Godfrey Hounsfield (1919-2004), an English electrical engineer, and Allan Cormack (1924-1998), a South African physicist
In 1979 Hounsfield and Cormack were awarded the Nobel Prize in Medicine and Physiology for the discovery of computed tomography

## Slide 32: History of CT
The research lasted in the period 1967.-1971.
In London, the first examination was carried out in 1971.
The first clinical research was done by neuroradiologist James Ambrose at the Mayo Clinic, USA

## Slide 33: Principles of work of CT
X-ray beam is passed at a cross section through a patients body
This eliminates superimposition
The beam is finely collimated this reduces scatter and gives better contrast resolution
The collimated beam pass through the body, the body tissue absorbs the beam

## Slide 34: Principles of work of CT
The beam exits the body and strikes the detectors
The detectors are quantitative and distinguish differences in tissue contrast
Detector converts photons to an analog signal
The ADC converts it to digital signal
Digital data is sent to CPU for reconstruction

## Slide 35: Principles of work of CT
CT enables the creation of images of transverse sections transverse to the longitudinal axis of the body using a collimated X-ray beam, which, passing through the object, is weakened due to absorption, and the intensity of the remaining part of the signal is registered by special detectors
The X-ray tube and detectors rotate synchronously around the object, in one plane
The absorption of X-rays depends on the atomic composition and density of individual tissues, as well as on the energy of X-ray radiation

## Slide 36: Image analysis
P - Pixel (picture element)
The smallest unit of a CT image.
Cross-sectional segment of the body
V – Voxel
Three-dimensional pixel - volume element
D – Layer thickness

## Slide 37: Hounsfield scale
The Hounsfield scale, named after Sir Godfrey Hounsfield, is a quantitative scale for describing radiodensity
It is frequently used in CT scans, where its value is also termed CT number
The Hounsfield unit (HU) scale is a linear transformation of the original linear attenuation coefficient measurement into one in which the radiodensity of distilled water at standard pressure and temperature (STP) is defined as 0 Hounsfield units (HU), while the radiodensity of air at STP is defined as −1000 HU

## Slide 38: Hounsfield scale
On the tomogram (CT section of the body) shown in gray scale, the attenuation (density) values of the tissue are measured
Density:
  Air -1000 HU
  Fat -120 to -90 HU
  Distilled water 0 HU
  Subdural hematoma +75 to +100 HU
  Bone +300 to +1000 HU

## Slide 39: Generations of CT machines
Sequential CT also known as step-and-shoot CT, or axial CT is a type of scanning method in which the CT table moves stepwise
The table increments to a particular location and then stops which is followed by the X-ray tube rotation and acquisition of a slice
Then the table increments again and another slice is taken
The table has to make a stop in taking slices
This results in an increased time of scanning

## Slide 40: Seqential CT

## Slide 41: Generations of CT machines
Helical CT (simultaneously with the rotation of the tube-detector system, the table for the patient moves as well)
Spinning tube, commonly called spiral CT, or helical CT, is an imaging technique in which an entire X-ray tube is spun around the central axis of the area being scanned
The main limitation of this type of CT is the bulk and inertia of the equipment (X-ray tube assembly and detector array on the opposite side of the circle) which limits the speed at which the equipment can spin

## Slide 42: Generations of CT machines
Multidetector row CT (MDCT) is the newer advancement in CT technology
The use of multiple detector rows allows faster scanning and thinner collimation
These improvements allow routine scans to be performed faster
MDCT enables CT angiography or virtual endoscopy

## Slide 43: Image reconstructions
Possibility of better topographical orientation
Multiplanar reconstructions (axial, sagital, coronal)
3D (three-dimensional reconstruction)
MIP (maximum intensity projection)

## Slide 44: Contrast CT
Contrast CT, or contrast enhanced computed tomography (CECT), is X-ray computed tomography (CT) using radiocontrast
Radiocontrasts for X-ray CT are generally iodine-based types
This is useful to highlight structures such as blood vessels that otherwise would be difficult to delineate from their surroundings
Using contrast material can also help to obtain functional information about tissues
Often, images are taken both with and without radiocontrast

## Slide 45: CT of the brain

## Slide 46: CT of the abdomen

## Slide 47: 3D reconstuction
pelvis temporomandibular joint

## Slide 48: CECT
aorta
pulmonary artery

## Slide 49: MAGNETIC RESONANCE IMAGING (MRI)

## Slide 50: MRI
Magnetic resonance imaging (MRI) is a medical imaging technique used in radiology to form pictures of the anatomy and the physiological processes of the body
MRI scanners use strong magnetic fields, magnetic field gradients, and radio waves to generate images of the organs in the body
MRI does not involve X-rays or the use of ionizing radiation, which distinguishes it from computed tomography (CT) and positron emission tomography (PET) scans
MRI is a medical application of nuclear magnetic resonance (NMR) which can also be used for imaging in other NMR applications, such as NMR spectroscopy

## Slide 51: MRI
MRI is widely used in hospitals and clinics for medical diagnosis, staging and follow-up of disease
Compared to CT, MRI provides better contrast in images of soft tissues, e.g. in the brain or abdomen
However, it may be perceived as less comfortable by patients, due to the usually longer and louder measurements with the subject in a long, confining tube, though "Open" MRI designs mostly relieve this
Additionally, implants and other non-removable metal in the body can pose a risk and may exclude some patients from undergoing an MRI examination safely

## Slide 52: History of MRI
Since its development in the 1970s and 1980s, MRI has proven to be a versatile imaging technique
The phenomenon of magnetic resonance was discovered in 1939. – Rabi
MR imaging was invented by Paul C. Lauterbur who developed a mechanism to encode spatial information into an NMR signal using magnetic field gradients in September 1971
Peter Mansfield further refined the techniques used in MR image acquisition and processing

## Slide 53: History of MRI
The first image of a section of human tissue was obtained in 1977. –Damadian
In 2003 Lauterbur and Mansfield were awarded the Nobel Prize in Physiology or Medicine for their contributions to the development of MRI
The first clinical MRI scanners were installed in the early 1980s and significant development of the technology followed in the decades since, leading to its widespread use in medicine today

## Slide 54: Basics of MRI
MRI was originally called NMRI (nuclear magnetic resonance imaging), but "nuclear" was dropped to avoid negative associations
Certain atomic nuclei are able to absorb radio frequency
(RF) energy when placed in an external magnetic field
The resultant evolving spin polarization can induce
a RF signal in a radio frequency coil and thereby be
detected

## Slide 55: Basics of MRI
In a strong magnetic field,
protons are oriented parallel
or antiparallel to the external field
lines of force of the magnetic field
in the coordinate system (X, Y and
Z axis)

## Slide 56: Basics of MRI
In clinical and research MRI, hydrogen atoms are most often used to generate a macroscopic polarization that is detected by antennas close to the subject being examined
Hydrogen atoms are naturally abundant in humans and other biological organisms, particularly in water and fat
For this reason, most MRI scans essentially map the location of water and fat in the body

## Slide 57: Basics of MRI
Pulses of radio waves excite the nuclear spin energy transition, and magnetic field gradients localize the polarization in space
By varying the parameters of the pulse sequence, different contrasts may be generated between tissues based on the relaxation properties of the hydrogen atoms therein
This is how we arrive at the selection of numerous sequences in which the examination of the patient can be performed

## Slide 58: Basics of MRI
In most medical applications, hydrogen nuclei, which consist solely of a proton, that are in tissues create a signal that is processed to form an image of the body in terms of the density of those nuclei in a specific region
Given that the protons are affected by fields from other atoms to which they are bonded, it is possible to separate responses from hydrogen in specific compounds

## Slide 59: Basics of MRI
To perform a study, the person is positioned within an MRI scanner that forms a strong magnetic field around the area to be imaged
First, energy from an oscillating magnetic field is temporarily applied to the patient at the appropriate resonance frequency
Scanning with X and Y gradient coils
causes a selected region of the patient
to experience the exact magnetic field
required for the energy to be absorbed

## Slide 60: Basics of MRI
The atoms are excited by a RF pulse and the resultant signal is measured by a receiving coil
The RF signal may be processed to deduce position information by looking at the changes in RF level and phase caused by varying the local magnetic field using gradient coils
The contrast between different tissues is determined by the rate at which excited atoms return to the equilibrium state
Exogenous contrast agents may be given to the person to make the image clearer

## Slide 61: T1 and T2
In a strong magnetic field, a new magnetic vector is established in the patient's body, the RF pulse creates transverse magnetization, and the longitudinal magnetization decreases
Each tissue returns to its equilibrium state after excitation by the independent relaxation processes of T1 (spin-lattice; that is, magnetization in the same direction as the static magnetic field) and T2 (spin-spin; transverse to the static magnetic field)
To create a T1-weighted image, magnetization is allowed to recover before measuring the MR signal by changing the repetition time (TR)

## Slide 62: T1 and T2
This image weighting is useful for assessing the cerebral cortex, identifying fatty tissue, characterizing focal liver lesions, and in general, obtaining morphological information, as well as for post-contrast imaging
To create a T2-weighted image, magnetization is allowed to decay before measuring the MR signal by changing the echo time (TE)
This image weighting is useful for detecting edema and inflammation, revealing white matter lesions, and assessing zonal anatomy in the prostate and uterus

## Slide 63: MRI today

## Slide 64: MRI today

## Slide 65: MRI today

## Slide 66: MRI today

## Slide 67: Bronchial carcinoma
Lung cancer is the most common cause of cancer-related death in both men and women
Four major cell types account for 95% of cases:
  adenocarcinoma
  squamous cell carcinoma
  large cell carcinoma
  small cell carcinoma
By localization there are 3 types of cancer:
  central tumours (75%)
  peripheral tumours (20-25%)
  Pancoast tumours

## Slide 68: Central tumours
The cardinal imaging signs of a central tumour are collapse/ consolidation of the lung beyond the tumour and the presence of hilar enlargement, signs that may be seen in isolation or in conjunction with one another
Obstruction of a major bronchus often leads to a combination of atelectasis and retention of secretions with consequent pulmonary opacity, but collateral air drift may partially or completely prevent these postobstructive changes
Hilar enlargement is a common presenting feature in patients with bronchial carcinoma
collapse RUL

## Slide 69: Peripheral tumours
Approximately 40% of bronchial carcinomas arise beyond the segmental bronchi, and in 30% a peripheral mass is the sole radiographic finding
The term corona radiata is used to describe numerous fine strands radiating into the lung from a central mass, sometimes with transradiant lung parenchyma between these strands
While not specific, this sign is highly suggestive of bronchial carcinoma
Absolutely spherical, sharply defined, smooth-edged nodules due to carcinoma of the lung are rare
Cavitation may be identified in tumours of any size and is best demonstrated by CT

## Slide 70: Peripheral tumours

## Slide 71: Neoplastic cavitation

## Slide 72: Corona radiata

## Slide 73: Pancoast toumors
A Pancoast tumor is a tumor of the apex of the lung (3%)
It is a type of lung cancer defined primarily by its location situated at the top end of either the right or left lung
It typically spreads to nearby tissues with localized destruction of ribs and vertebrae
Most Pancoast tumors are non-small-cell lung cancers
The growing tumor can cause compression of a sympathetic ganglion (the stellate ganglion), resulting in a range of symptoms known as Horner's syndrome (ptosis, miosis, anhidrosis)

## Slide 74: Pancoast toumors

## Slide 75: Bronchiolo-alveolar carcinomas
Bronchiolo-alveolar carcinomas arise from the alveoli and the immediately adjacent small airways
They therefore present as peripheral pulmonary opacities rather than with the effects of large airway obstruction
The most common radiographic finding is a solitary lobulated or spiculated pulmonary mass indistinguishable from other types of carcinoma
Bubble-like lucencies corresponding to patent small bronchi, air-containing cystic lucencies, or air bronchograms and cavitation may be seen

## Slide 76: Bronchiolo-alveolar carcinomas

## Slide 77: Metastases
Pulmonary metastases in adults are usually from breast, gastrointestinal tract, kidney, testes, head and neck tumours or from a variety of bone and soft tissue sarcomas
The spread of extrapulmonary neoplasm to the lung may occur by direct invasion of the pulmonary parenchyma or as a result of hematogenous dissemination
Direct invasion of the lung may occur with mediastinal, pleural, or chest wall malignancies
  The most common mediastinal malignancies to invade the lung are esophageal carcinoma, lymphoma, and malignant germ cell tumors, or any malignancy metastasizing to mediastinal or hilar lymph nodes
Hematogenous metastases to the lung may be seen with any tumor that gains access to the superior vena cava, inferior vena cava, or thoracic duct, because the pulmonal artery is the final common pathway for these channels

## Slide 78: Metastases
Pulmonary nodules are the most common manifestation of hematogenous metastases to the lung
They are most commonly seen in carcinomas of the lung, breast, kidney, thyroid, colon, uterus, and head and neck
Carcinomas of the rectosigmoid colon, osteogenic sarcoma, renal cell carcinoma, and melanoma are more likely to result in solitary pulmonary metastases
Lymphangitic carcinomatosis (LC) - while direct parenchymal lymphatic invasion and obstruction of hilar and mediastinal lymph nodes by bronchogenic carcinoma is the most common cause of unilateral LC, extrapulmonary malignancies may invade pulmonary lymphatics after hematogenous dissemination to both lungs to produce interstitial deposits of tumor
In LC, the tumor cells invade the lymphatics within the peribronchovascular and peripheral interstitium, resulting in lymphatic dilatation, interstitial edema, and fibrosis
The most common extrathoracic malignancies to produce LC are carcinomas of the breast, stomach, pancreas, and prostate

## Slide 79: Metastases
multiple nodular metastases (hematogenous)

## Slide 80: Metastases

## Slide 81: Metastases
Lymphangitic carcinomatosis

## Slide 82: Golden S sign
central bronchial carcinoma + atelectasis

## Slide 83: Pleural tumours – mesothelioma

## Slide 84: Mediastinal tumours
lymphoma fibrosarcoma

## Slide 85: Liver tumors
Hepatocellular carcinoma (HCC)

## Slide 86: Liver metastases

## Slide 87: Pancreatic adenocarcinoma

## Slide 88: Renal cell carcinoma (RCC)

## Slide 89: Bladder cancer

## Slide 90: Rectal cancer