## Slide 1
University of Kragujevac The Medical Faculty Integrated Academic Studies of Medicine Physical medicine and rehabilitation
Module 1
Lecture 4
ELECTROTHERAPY -Alternating currents-
Docent Dr. Igor Simanic

## Slide 2
ALTERNATING CURRENTS
change
      Of intensity and
      Direction of ion flow

## Slide 3
Farad current
Faraday 1831
  asymmetry,
  irregularity of a cycle
  only historical importance

## Slide 4
Technique of application
Stable method
Bipolar technique with metal plate electrodes
Labile method
Monopolar technique. Active electrode is in a shape of a cyllinder or in a shape of a bigger or smaller brush.

## Slide 5
Neofarad current
  Impulse 1 ms,
  Pause 20 ms and
used for diagnostic purposes

## Slide 6
Neofarad current
Has a stimulative effect on the sensory and motor nerves (tetanic contraction).
It is used:
In classic electrodiagnostics
As labile faradization in psychogenic disorders (hysteria and enuresis)

## Slide 7
Transcutaneous electrical nerve stimulation (ТЕNS)
Impulses
Usually in an array of impulses of 7 or more very short impulses.
Impulse lasts from 0,05 to 0,4 ms, and the frequency is from 75 to 125 Hz.
Impulses are triangular or rectangular, biphasic or monophasic

## Slide 8
Transcutaneous electrical nerve stimulation (ТЕNS)
Еlectrostimulation for pain management
“gate control" theory
Presence of endogenous opioid and non-opioid system in achieving the analgesic effect: endorphins and enkephalins

## Slide 9
Middle-frequency currents
Interferential (Nemec’s) currents
Sinusoid-modulated currents (Russian stimulation)

## Slide 10
Interferential currents (IFC)
IFC are low-frequency alternating currents of a sinusoidal shape which occur endogenously in the tissues, by interference (superposition) of the middle-frequency currents from two independent circuits, which differ in frequency from 0-100 Hz.
IFC are obtained by crossing power lines of two middle-frequency circuits which have a different frequency and the same strength. By phenomenon of interference, at a site of crossing, bio-power is obtained, whose frequency amounts to the difference in frequency of the component currents, that’s why they are called “crossed currents”.

## Slide 11
Interferential currents (IFС)
Frequency of one circuit (А) is always constant and amounts to 4000Hz. The other circuit has a variable frequency which amounts from 3900 to 4000Hz or 4000 to 4100Hz (B).
The obtained current- IFC (C) can be constant or rhythmically variable within the range from 0 to 100Hz.
Besides its frequency, a current changes its intensity of interference from maximal interference (100%) to 0 and vice versa.

## Slide 12
Physiological effect of ICC
from 1 to 10 Hz - stimulatory effect on the neuromuscular system, causing muscle contractions.
from 1 to 50 Hz - stimulatory effect
from 1 to 100 Hz highly trophic effect, antiedematous, analgesic effect
From 60 to 100 Hz stimulate bone healing
Current with a rhythmic frequency from 90 to 100 Hz has sympaticolytic and analgesic effect.

## Slide 13
The summed biological effects of ICC
Stimulatory on the blood flow, causing vasodilation, which leads to the increased blood flow and oxygenation of the tissues, as well as faster toxin and pain mediator elimination.
Analgesic, because of improved circulation and oxygenation of the tissues and the effect it has on nerve endings.
Increased excitability and conductability of the peripheral nerves, which has a stimulatory effect on the damaged nerves.
Inhibitory effect on the sympaticus and stimulatory on the parasympaticus.
Increase of the lymph flow and the resorption of edema.
Improved muscle mass, and promoted wound healing.
Stimulated formation of callus in fractures.
Change of pH value towards the alcalinity.
Anti-inflammatory, increasing circulation, metabolism and resorption.
Stimulatory on the transversely-striated and smooth muscle fibers.

## Slide 14
Dosing of IFC
Strength of a current (mА) - subjectively
Frequency (Hz) – according to a diagnosis
Duration of the application time: 10 to 30 minutes.
Number of treatments: not limited

## Slide 15
Indications for IFC
Post-traumatic conditions (contusion, distortion, luxation...)
Bone fractures and its complications (pseudoarthrosis, Мb. Sudeck...)
Cervical and lumbar syndrome, neuralgia, neuritis...
Conditions after the nerve injuries
arthritis, arthrosis, Мb. Bekhterev, PAHS, rheumatoid arthritis, non-articular rheumatism
Mb. Burger, Мb. Raynaud...

## Slide 16
High-frequency current
Is an alternating current with a frequency over 300 kHz. HFC represents a specific form of thermotherapy, which uses heat, obtained by conversion of electrical power, to be absorbed by tissues.
Тhe heat produced this way in the organism is called endogenous heat, because it is developed in the tissues themselves, unlike the exogenous heat, which acts externally on the skin.

## Slide 17
HFC Short-wave diathermia
wavelength
22,12 m/ 11,06 m
frequency
13,56 МHz /27,12 МHz

## Slide 18
Effects of HFC
Primary effect - thermal
Secondary effects

## Slide 19
Secondary effects of HFC
On circulation
On the nervous system
On muscles
On connective tissue
On metabolism and enzyme activity
Bacteriostatic and bactericidal effect

## Slide 20
Electrodes for SWD and methods of use
  Chalcogenide glass electrodes (electric)
  Plate, rubber electrodes – Rabb’s electrodes (magnetic field)
  Coil of an electrode: monode and minode
  Induction cable or line

## Slide 21
Dosing
Dosing of intensity is performed in watts and maximal dose is up to 100W.
Dose is usually determined based on the subjective patient’s feeling, whereby pleasant and mild warmth should be felt.
Depending on the radiation intensity, the following doses may be applied:
    Athermal, when warmth is not felt
    Oligothermal, when only mild warmth is felt
    Thermal, when pleasant warmth is felt and
    Hyperthermal, when strong warmth is felt.
Duration of the application time is from 15 to 20 minutes.

## Slide 22
Indications for SWD
Rheumatic diseases in chronic stage.
Conditions after the injury of the locomotive apparatus (except the acute ones)
Nerve diseases (neuralgia and neuritis)
Chronic diseases of ear, nose and throat (sinusitis, otitis),
Gynecological chronic non-specific inflammatory diseases (adnexitis, parametritis, salpingitis, adhesions after gynecological surgeries, primary and secondary sterility
Chronic non-specific pulmonary diseases (chronic bronchitis, after pneumonia and exudative pleuritis, lung abscess)
Skin diseases: furunculosis, carbuncle, hydroadenitis
Nerve diseases (neuralgia and neuritis)

## Slide 23
Contraindications for SWD
Acute inflammations,
Febrile conditions,
Malignant tumors,
Tuberculosis,
Bleeding tendency
Menstruation
Metal objects at the site of application,
Pregnancy (cave abortus),
Obliterating endarteritis,
Unadequate sensory response to thermal stimuli

## Slide 24
Precautionary measures!!!
pace-maker
wooden bed or wooden chair
metal
hearing aid and watch
metal implants
cables