## Slide 1
ORTHOSES AND THEIR USE IN THE MUSCULOSKELETAL REHABILITATION
Doc. Dr. Igor Simanic
Doc.dr Igor Simanić
ORTHOSES AND THEIR USE IN THE MUSCULOSKELETAL REHABILITATION

## Slide 2
Orthos is a Greek word meaning “straight.“ This is how an orthosis got its name; it is a device which keeps a body segment in a straight position, corrects that position and assists the body segment performing the functions. Today, the name orthosis is used for various devices covering different parts of the body. Also, the names “brace” or ”splint” have been used increasingly.
International organization for standardization defined orthoses as externally applied devices which correct structural and functional characteristics of the neuromusculoskeletal system. Orthoses are orthopedic appliances that apply force to support, align, prevent or correct deformities of a body part or improve the function of a movable body part.

## Slide 3
In any case, an orthosis as an exoskeleton that must have at least one system of fixation with three contact points per body segment. The same rule applies to the activity-specific units which are used as additions. Also, other important factors include proper prescription, as well as precise manufacturing with the use of high-quality and durable materials, the adequate training and gaining experience in its use.

## Slide 4
Depending on the place of application, orthoses are classified into groups for upper extremities, for lower extremities and the spine. They are more precisely defined by body segments or joints they cover, and in the end, by their function.
A unique protocol has not been created so far to include indications, standards, nomenclature, precise descriptions of certain parts and systems, considering the elements of the functional deficit, physiology, anatomy, biomechanics of certain systems and material specification.

## Slide 5
Orthoses for upper extremities
All orthoses for upper extremities are based on the basic opponens orthosis, onto which other components are fitted for the purpose of managing specific individual impairments. In the prescription of the upper extremity orthoses, an analysis of orthotic function is used. It is used to determine the components of the function deficits in terms of the spinal stability, hand position and the potential for grasp and release activities.
For achieving the spinal stability, slings and gravity-balanced orthoses are used. Further arm positioning is achieved with the use of orthoses for shoulder, elbow, wrist and hand (SEWHO), such as Ultra-Lite orthosis. It can be mounted on all types of wheeling chairs, it is height-adjustable and unburdens or fixes certain parts of the arm during the recovery phase.

## Slide 6
For subluxation and instability of the shoulder joint, better results are achieved with the use of shoulder orhoses than by surgical treatment. Non-traumatic shoulder subluxation occurs as a consequence of the brachial plexus lesions, as well as in hemiplegia, and both are treated the same way.

## Slide 7
Shoulder immobilizer. It is used in a shoulder luxation and a proximal humerus fracture, as well as postoperatively.

## Slide 8
For stabilization of this region, a brace for a clavicular fracture can be used, with shoulder pelotte or a scapular protecting brace and posture correcture.
Recently, there has been a new subgroup of immobilization orthoses for post-traumatic and post-surgical humerus conditions.
Brace for a clavicular fracture with shoulder pelottes or a scapular protecting brace and posture corrector.

## Slide 9
Elbow orthoses (EOs) as monoarticular orthoses account for 7% of a total number of the upper extremity orthoses. The most common indications for the use of these orthoses are epicondylits (golf and tennis elbow), contractures, neurological disorders, elbow instability and post-traumatic and postoperative interventions. The orthotic use is most often connected with lateral epicondylitis of the humerus, with an incidence rate of 3%.

## Slide 10
Contractures of the elbow joint as consequences of the structural changes of the non-osseous tissues can be treated with compression splints, elastic splints or an orthosis with a small amount of constant pressure on extension.

## Slide 11
Elbow-wrist orthoses (EWOs), such as Thamert orthosis, are longer than elbow orthoses. Modified to include an elbow unit and epicondylar pelottes, it is known as an orthosis for tennis elbow. Indications include tendinopathy, intraarticular lesions, radial nerve compression and cervical radiculopathy.

## Slide 12
WRIST AND HAND ORTHOSES

## Slide 13
There is a large number of specific-activity orthoses such as Cock up Splint Half for dorsiflexion of the wrist and Thumb Spica splint with a thumb fixation. Grip-Fit splint and AliDry splints are used for the carpal tunnel syndrome and allow for a full grasp force with control of dorsiflexion.

## Slide 14
Wrist, hand and finger orthoses (WHFOs) are used in arthritis and postoperative conditions. Thera Plus orthosis has a thumb abductor and finger separators, while Thera-Flex with T profile is used for treating spasticity, and allows adjustments.

## Slide 15
The treatment of metacarpophalangeal and intraphalangeal joint contractures includes the use of Base Ball, E-Z Flex and Air System orthoses.

## Slide 16
Lower-limb orthoses
Neurological indications for the use of orthoses are connected with pathological conditions of n. femoralis and n. sacralis. The motor deficits are present in the lesions of plexus sacralis (pelvic fractures, stab and gunshot wounds, tuberculosis, malignant pelvic tumors), lesions of the n. ischiadicus, n. peroneus communis, the fibular neck fractures (direct trauma), fractures and compressions. In rheumatology, the orthotic treatment has the following indications: arthritis, osteoarthrosis genum, periarthritis genum and osteoporosis.
Traumatic indications for orthotic treatment include distorsions and luxations of the knee, lesions of the ligamentous knee apparatus, injuries of the menisci, fractures of the femoral condyles, fractures of the tibial plateau and luxation fractures, ankle distorsions and malleolus fractures.
Diseases and deformities requring an orthotic treatment include angular deformities of the knee, genu valgum and genu varum, genu flexum, genu recurvatum, gonitis tuberculosa, Mb. Osgud-Schlatter, external or internal tibial torsion, tabetic artropathy – Charchot joint, osteochondritis dissecans, osteomyelitis and leg length discrepancy.
.

## Slide 17
Besides standard hip orthoses (Hos), the recent advances include Zetton Band hip orthosis for prevention of dislocation after total hip arthroplasty and Dina Cox orthosis which secures the femoral head tightly in the acetabulum.

## Slide 18
Knee, ankle and foot orthoses (KAFOs) have the highest rejection rate among patients.The rejection rate is between 58-79% and generally, 40% of users are dissatisfied.

## Slide 23
Ankle and foot orthoses (AFO).

## Slide 25
Spinal orthoses
Spinal orthoses are used to reduce pain, protect from further injuries, support weak muscles and prevent or correct a deformity. This is achieved through biomechanical effects of the trunk support, movement control and realignment of the spine.
The muscle weakness and atrophic changes, contractures in the immobilized region, psychological dependence and increase of the energy cost during walk are negative aspects of the spinal orthtotic treatment.
The nomenclature of spinal ortoses is rather confusing. It is used for classification according to the level of the spine being treated.

## Slide 26
Spinal orthoses
Body’s mid-line runs down from the middle of the ear, through the shoulder joint, passes the knee and stops at 2cm from the ankle.

## Slide 27
Cervical orthoses
The role of the cervical orthoses is to provide support and protection and to limit the mobility. Cervical orthoses are most efficient at limiting the flexion and extension, because even with the most efficient cervical orthoses, lateral flexion can be limited only up to 50%,and rotation only 20% of the normal range of movement. The movements in the sagittal plane are better controlled.

## Slide 28
Semirigid collars such as Miami J and Aspen.
Malabu - Miami J
Soft cervical collars offer the restriction of movement more through a sensory feedback than through an actual mechanical restriction of movements. They can be enforced with a plastic stiffener. They are used for torticolitis, rheumatism and conditions of excessive strain.

## Slide 29
Firm cervical collars are made with the anterior and posterior plastic rigid supports. Philadelphia or CTO Aspen 2-4 collar restricts the movements in the anteroposterior direction up to 30%, allows for 43% of rotation and 67% of lateral flexion. They are used for stabilization, pain management and postoperative conditions. They can have an opening for a tracheostoma.
Aspen 2-4
Philadelphia
Cervical immobilizer

## Slide 30
Rigid polyethylene collar with the mandibular and occipital support offers a similar effect, but it can be uncomfortable because of the main support which is placed on the clavicles. The most commonly used orthosis of this type is Thomas collar.

## Slide 31
For lesions of the spinal cord, other type of orthoses is used: sterno-occipitomandibular immobilizer (SOMI). It is an easily applied orthosis of light weight, which allows very small amplitudes of movement. This group also includes an adjustable orthosis for torticolitis intended for an early postoperative period after a surgical correction.
Cervical orthosis “Four-post collar”

## Slide 32
Cervicothoracic orthoses (CTOs) are efficent for the restriction of the neck movements in the sagittal plane. The most common types include Jonson and Jewett orthosis. The main feature of these orthoses is that the lowest point of support is placed on the thoracic segment.

## Slide 33
Cervical orthoses with the total contact are Minerva and HALO. The Minerva type is grouped as a mandibulo-occipito-sterno-thoracic orthosis. This type of orthosis provides a complete restriction of the lateral flexion and rotation. HALO-type of orthosis is indicated for the treatment of quadriplegia because of its efficacy in preventing all neck movements.
HALO

## Slide 34
Thoracic-lumbo-sacral orthoses
The efficacy of these orthoses is seen in the combination of unburdening and restriction of the trunk and intervertebral body movements. The positioning of the spine is obtained through the muscle contraction, and in a smaller degree, passively, through an orthosis.
The types of these orthoses include lumbostad corsets, firm unburdening orthoses, hyperextension unburdening orthoses and corrective orthoses.

## Slide 35
The corsets are made of a firm fabric, with the steel bar supports on the posterior side. They can be lumbosacral or thoraciclumbosacral.
Thoracic orthoses for sternal fracture

## Slide 36
Inadequate posture, weakness of the thoracic musculature
TLS
Posture and shoulder control

## Slide 37
LSP
LS

## Slide 38
Lumbostad corsets have increasingly been used. Their role is to stabilize and unburden the lumbosacral part. They are used for management of acute and chronic back pain.

## Slide 39
Lumbostads with various level of support.

## Slide 40
Rigid unburdening orthoses also include a lumbosacral orthosis ( LSO), the type of an unburdening orthosis with the back support or frame (Chair Back brace, Frame Back brace and Clamshell brace). This type of orthosis controls the movements of flexion and extension, as well as lateral movements of the lumbar spine.
Clamshell LSO
Chair Back

## Slide 41
Hyperextension unburdening orthoses are indicated in the vertebral fractures without neurological deficits when a surgical intervention is not necessary. The function is provided through a sternal, symphysal and lumbar pelotte.
Tynor's Ash

## Slide 42
In the moderately severe compression fractures of the vertebral bodies, Jewett and Cash types of hyperextension orthoses are used.
Tynor's Ash
Jewett

## Slide 43
In the treatment of the severe compression fractures, the imperative for an orthosis is to offer a sagittal hyperextension through a three-point system of support, restrict trunk movements and reduce the segmental motion of the vertebrae in all three planes. It is achieved by applying a TLSO corset with a total contact in hyperextension.
Clamshell TLSO

## Slide 44
The treatment of compression fractures in osteoporosis includes a special type of orthosis.
Fracture in osteoporosis

## Slide 45
Orthosis for osteoporosis
Points of orthotic impact

## Slide 46
Corrective orthoses
The orthotic treatment is the most-often used non-surgical method in the treatment of adolescent idiopatic scoliosis (AIS). In the non-surgical treatment of adolescent idiopatic scoliosis, the spinal orthoses achieve the best results. They make a compromise between a patient's quality of life and the inevitable factors such as physical restraint, unseemly appearance and psychological issues.
Increased muscular activity on the convex side,
Elevated shoulder on the convex side,
Raised scapulla on the convex side,
Head tilted towards the concave side
skolioza
skoliosis
normal spine

## Slide 47
Corrective orthoses
The orthotic treatment is the most-often used non-surgical method in the treatment of adolescent idiopatic scoliosis (AIS). In the non-surgical treatment of adolescent idiopatic scoliosis, the spinal orthoses achieve the best results. They make a compromise between a patient's quality of life and the inevitable factors such as physical restraint, unseemly appearance and psychological issues.
The best-known corrective corset was made by Blount and Schmidt in 1940, a so-called Milwaukee corset which belongs to the group of rigid cervico-thoraco-lumbo-sacral orthoses (CTLSO). It is indicated in juvenile scoliosis greater than 20adolescent from 25 to 45 and
the curves above the Th8 (Th7) level. This corset is worn for 24 hours, and it can be removed after the fusion of the ring apophyses of the vertebral bodies and is conducted gradually through the period of two years.

## Slide 48
The most commonly used are cervico-thoraco-lumbo-sacral orthoses (CTLSOs). The corsets which allow a certain degree of motion and do not involve the cervical spine include Boston, Charleston, Providence, Cheneau, Wilmington, Miami, Rosenberger, Lyonnaise etc. which bear their name after the center in which they have been designed.
Rosenberger
Wilmington
CTLSOs

## Slide 49
Boston TLSO belongs to the group of the underarm corsets and is the most frequently prescribed brace in North America.

## Slide 50
TLSO corset allows for physiologica movements (rotational, translational and axial) and restricts the unwanted movements.

## Slide 51
A more recent type of TLSO corset is the Charleston corset which efficiently corrects single curves from 25 do 35. The conditions after the surgical spine fusion involve the use of Bi-Valve TLSO orthosis.
Bi-Valved TLSO

## Slide 52
The first flexible spinal orthosis (Dynamic Corrective Brace, SpineCor) was made in 1980 by Coillard and Rivard. SpineCor allows movements within the corset. This orthosis was defined as elastic; it can provide a constant pressure which controls the posture when a patient is relaxed.
The main role of corrective orthoses is to prevent further progression of deformities, while they also have a smaller effect on the correction of deforimity.
From a biomechanical point of view, the combined effects of support, lateral detorsional pressure and the curve correction provide stabilization of an orthotically treated scoliotic spine. The effectiveness of orthotic treatment depends on the performances of an orthosis, as well as the constant monitoring and orthotic adjustments.

## Slide 53
Conclusion
The role of orthoses is reflected in the control of movements, deformity correction or compensation for the weakness of muscles or ligaments.
Control of movements implies a complete prevention of movements and restriction of the range of motion to the normal or partially normal range of motion.
The prevention of deformity development or recurrence is provided by structural orthoses, while dynamic orthoses compensate for the weakness of muscles or group of muscles.
Orthotic rehabilitation is an integral part of restoration of functionally insufficient persons.

## Slide 54
For an orthosis to be approved by an expert and accepted for use by a patient, it has to meet multiple requests. It must help a patient to perform some activity, to enable him to do as many activities as possible, it should be of light weight, and easy for taking on and off. The prescription of orthotic devices should be done individually, considering the technical possibilities and also the level of functional deficit and biomechanical parameters.