## Slide 1: surgical TREATMENT OF FRACTURES
Asst. Professor Željko Stepanović, orthopedic surgeon,
Clinic for Orthopedics and Traumatology of UCC Kragujevac,
Faculty of Medical Sciences, University of Kragujevac
28 th week IAMS

## Slide 2: content
INTRODUCTION
MODALITIES OF OPERATIVE TREATMENT OF FRACTURES
BIOMECHANICS OF FRACTURE HEALING
TYPES OF INTERNAL FIXATION
ADVANTAGES OF INTERNAL FIXATION
DISADVANTAGES / COMPLICATIONS
EXTERNAL FIXATION
ADVANTAGESOUTSIDEASH FIXATIONS
DISADVANTAGES / COMPLICATIONS

## Slide 3: INTRODUCTION
Operative treatment of fractures dates back to the 19th century
1865 - Louis Pasteur
1867 - Joseph Lister
Development of metallurgy in the 20th century
1939 - V nail
1958 -AO school
1970-Gustilo-Anderson
2003-Biological plating-LCP concept AO school

## Slide 4: Fracture treatment modalities
According to the treatment time for injuries of the bone-joint system, we differentiate
Urgent Care (ATLS)
Primary management of fractures (DCO)
Definitive management of the fracture

## Slide 5: GOAL OF SURGICAL TREATMENT
Establishing the anatomical shape of the joint
Establishing bone axis / length
Establishing a normal load distribution
Early activation and prevention of post-traumatic OA
Notes: Speak of osteosynthesisnot yespermanently replacefunction brokenboneand
Osteosynthesis shouldto provide a temporaryinsupportin a broken bone in the biomechanical sense and its healing in responseravishing anatomical position.
Establishmentanatomical shape of the joint
Establishment axles/ length bones
Establishmentnormaledistributione workload
Rana activationandprevention of post-traumatic OA

## Slide 6: Treatment protocol
Radiographs / CT allow adequate fracture classification
Location of fractures,dislocation and instability determine the need for surgical treatment
Fracture type ("fracture personality") determines the surgical approach
Individual approach in the treatment of fractures and patients
Notes: Radiographs/CTenable adequate classification fractures
Location fractures,dislocation and instability determine need For surgical treatment
Typefractures ("fracture personality")determines surgical access
Individual access intreatment certain fractures and patients

## Slide 7: INDICATIONS FOR Operative treatment
Open fractures
Polytrauma
Intra- articular fractures
Vascular injury
Nerve Injury
Closed unstable fractures
Pathologic fractures
Bleeding
Early mobilization
Notes: Urgenthsurgical cases include:
Openedand fractures acetabulummind.
Newly created paralysis ischiasciatic nerve afterclosede reductione dislocations hook.
Notreposable last dislocation hook.
Central dislocation heads thigh bones according to spongy bone surface inrighttnog ilium.

## Slide 8: CONTRAINDICATIONS FOR SURGICAL TREATMENT
Operative contraindications:
Local or systemic infection
Poor local skin status
Relative contraindications:
Very old patients
Pronounced osteoporosis
Comorbidities
Severe associated injuries
Polytraumatized patient unstable for major surgery
Limited surgical experience
Absence of adequate technical support
Notes: Operativeno contraindications:
Pronounced osteoporosis
Local or systemic infection
Poor local skin status (morel-Lavallélesion)
Relative contraindications:
Very old patients
Comorbidities
Severe associated injuries
Polytraumatized patient unstable for major acetabular surgery
Limited surgical experience
Absence of adequate technical support

## Slide 9: Advantages of internal fixation
Obtaining anatomical reduction of the fracture
Stability in the fracture zone (absolute/relative)
Sparing of soft tissues
Early mobilization and support
Higher % healing of unstable fractures without malposition

## Slide 10: Disadvantages of internal fixation
Implants do not induce fracture healing
Implant / bone fracture
Possibility of infection of the operative site
Fracture after implant removal
Discomfort from implants
(subcutaneous position, pain in the entry zone during IM nailing, etc.)

## Slide 11: fracture types
Fracture patterns occur based on the manner, magnitude, and speed of force applied to the bone
Bending load → transverse fractures without/with wedge segment
3-point bending → wedge segment fracture
4-point bending → segmental fracture
Torsional loading → oblique or spiral fracture
Axial load → articular impact fracture (plateau T, pylon T, etc.)
Notes: Figure from: Schatzker J, Tile M: ​​The Rationale of Operative Fracture Care. Springer-Verlag, New York, p. 3, 1987.

## Slide 12: Biomechanics of fracture healing
Fracture healing:
primary (osteonal)
secondary (callus)
When treating a fracture, the following should be taken into account:
Personality of the patient
Fracture feature
Stress is defined as the change in fracture diameter divided by the initial diameter (ΔL/L).
The stress within the fracture crack determines the type of healing.

## Slide 13: Principles of the AO School in 1958
Primary bone healing
Anatomical reduction.
Fixation: absolute stability
Preservation of supply blood
Early active mobilization without pain

## Slide 14: Primary (directly) bony healing
IF and intimate cortical contact with screws and/or plate and screws to achieve:
conditions of absolute stability between fragments
interfragmentary crack ≤ 200µ
stresses between fragments < 2%
direct (osteonal) healing without callus (cutting cone)

## Slide 15: Principles of the AO School today
Secondary biological healing
Reduction: restore anatomical relationships
Fixation: absolute or relative stability
conditioned by the peculiarity of the fracture
Preservation of vascularization of bone tissue and periosteum (soft tissue covering)
Early and safe mobilization
Notes: After more than 50 years, the four principles are almost the same, having withstood the test of time.
References:
Rüedi TP, Buckley RE, Moran CG.AO Principles of Fracture Management.2nd ed. Stuttgart, New York: Thieme Verlag; 2007: vol 1.1.1-6.

## Slide 16: Secondary(biological) bony healing
There are:
conditions of relative stability between fragments
present interfragmentary movements
strains between fragments 2% -10%
4 stages of healing:
Hematoma/inflammation/ IL-1β / BMP
Soft callus (3rd week)
Hard callus (weeks 6-8)
Reconstruction (remodeling) 2-10 years

## Slide 17: Biology of bone healing
Primary / direct bone healing
Joint fractures
Simple fractures
Open reduction and internal fixation of fractures (ORIF):
Lag screws
Plates and screws
Secondary/Indirect bone healing
Complex fracture types
The fracture is seen indirectly (fluoroscopy)
Indirect fracture reduction and fixation:
  IM nails
  Fracture bridging plates
  External fixation
Notes: Most fixations probablyincludes components of both typeshealing.
Even in excellent situationsUF and absolute stability fragments can seesmall degree formedme callus(II healing).

## Slide 18: TYPES OF FRACTURE FIXATION

## Slide 19: Internal Fixation
Closed reduction and percutaneous pin fixation (ZRPF)
Interfragmentary - engaging screws (lag screw)
Plate constructions - screws
Tension band – the principle of the tension band
Intramedullary nails (F / T / H)

## Slide 20: Closed reduction and percutaneous fixation
Fractures that do not require open reduction
Often used in the treatment of operative pediatric trauma Example 1: Pediatric supracondylar humerus fracture
The most common surgical fracture in pediatrics
Urgent surgical treatment for neurovascular problems

## Slide 21: Closed reduction and percutaneous fixation
Minimally dislocated femoral neck fractures
Reduction with the help of a special OP table for the treatment of fractures
Percutaneous cannulated screws for fixation

## Slide 22: Percutaneous osteosynthesis with Plate-MIPO
Placement through modified incisions
Indirect reduction techniques
Limited incision for: Passage and plate placement
Individual screw placement
Soft tissue "friendly"

## Slide 23: Osteosynthesis screw
The screw is the basic and most effective tool for internal fracture fixation, especially in combination with plates.
A screw is a powerful tool that converts rotation into linear motion, friction and compression forces.
Field of application: cortical, spongy, bicortical, monocortical, malleolar.
Function: Pulling Screw, Head Locking Screw, Position Screw, Transfixation Screw, Anchor Screw, Poller Screw, etc.)

## Slide 24: Osteosynthesis screw
Conventional DCP plates
Screws apply compression to the bone
The friction of the bone-plate construction creates stability
Axial compression at the contact of fragments
Threaded heads locked in LCP plate
Angularly stable construction
The screws are fixed in the plate
No contact or friction of the bone-plate construction is required for stability
Osteoporotic fractures
Locking screws
Conventional screws
Notes: The interface between a locking head screw and the plate will not loosen. Interfragmentary compression is not possible using locking head screws, nor is compression of the plate to the bone.
Shear = lateral deformation produced in a body by an external force, expressed as the ratio of the lateral displacement between two points lying in parallel planes to the vertical distance between the planes.
Conventional screws create compression between the plate and the screw. The plate is compressed onto the bone and it is this friction that conveys stability to the fracture site.
Locking head screws put the plate under shear. There is a space between the bone and the plate. No compression of the plate onto the bone is achieved. Screw loosening does not occur at the screw-plate interface.

## Slide 25: Plates for osteosynthesis

## Slide 26: Plates for osteosynthesis
Plates behave like internal splints.
Load bearing implants
IF plates can be used to achieve:
absolute stability
relative stability
Different anatomical locations require different shape and plate sizes:
precontoured plates

## Slide 27: FUNCTION OF PLATE FOR OSTEOSYNTHESIS
The plate design has evolved to meet the needs of the patient.
A surgeon, not the plate designer, determines how the plate will function and how it will be implemented.
Same plate: different BM functions.
There is a plate 6 mechanical functions:
Protection/neutralization
Compression
Tension band
Bridging
Buttress
Reduction

## Slide 28: Plate design for osteosynthesis
The compression of the DCP plate on the bone has a biological consequence of greater damage to the periosteum in relation LC-DCP.
All plates should be applied with respect to the preservation of soft tissues -"biological plating"
Notes: Studies have shown that the blood supply under a fixed dynamic compression plate showed poor periosteal blood supply leading to bone necrosis and absorption with a potential for delayed union and infection.
The low-contact DCP was developed to reduce the plate-bone contact, leaving the periosteal blood supply less disturbed with less bone necrosis.

## Slide 29: PLATE FUNCTION FOR OSTEOSYNTHESIS
Neutralization plate: neutralizes the forces of bending and rotation to protect the fixation of the lag screw
Dynamic compression plate: screw position allows axial compression in the fracture zone
Tension band:The plate is attached to the tension side of the fracture and converts the tensile force into a compressive force in the cortex opposite the implant.
ButtressThe plate resists the axial load by applying a force at 90 ° to the axis of potential deformation
Bridging:The plate provides relative stability by attaching to the two main fragments, achieving the correct length, axis and rotation. The fracture site remains intact
Reduction:The plate helps in the direct reduction and overall placement of fragments that are either temporary or definitive.

## Slide 30: Neutralizing Plate
Neutralizes / protects screws in the fracture zone from forces:
shearing
bending
torsion
"Protective plate"

## Slide 31: DYNAMIC COMPRESSION PLATE
Absolute stability
Direct healing
Transverse or Oblique fractures Fractures"A/B"
The screw compresses the plate to the bone
The oval screw hole design allows the screw position to achieve axial compression in the fracture zone
Notes: Axial compression can only be achieved using the DCP if the fracture is simple transverse or short oblique. In short oblique fractures the plate must be fixed to the bone so as to create an axilla between the plate and bone into which the second fragment can be drawn.

## Slide 32: COMPRESSION WITH A PRESTRESSED PLATE
Prestressed plate
A small convexity on the plate centered on the fracture
The plate is applied prestressed and as the plate is compressed to the bone, the plate straightens and forces the opposite cortex into compression
The proximal cortex is compressed using standard methods (DCP).
External compression device
Notes: Alternatively, a Verbrugge clamp over a screw can be similarly used to promote compression.
Figure from: Schatzker J, Tile M: ​​The Rationale of Operative Fracture Care. Springer-Verlag, New York, p. 9, 1987

## Slide 33: BUTRESS PLATES
They "support" the bone
It resists shear forces during axial loading
It is used in metaphyseal areas to support intra-articular fragments
The plate must conform to the contours of the bones to really achieve a supportive effect

## Slide 34: BRIDGING PLATES
"Bridging" / bypassing comminution
The goal of proximal and distal fixation is to maintain:
The length
Rotation
Axial shaft
Avoid damage to soft tissues in the fracture zone and allow vascularization in the same zone

## Slide 35
Notes: Relative stability heals with callus.

## Slide 36: PRINCIPLE OF TENSION BAND WITH PLATE
The plate is attached to the tension side of the fracture and converts the tensile force into a compressive force in the cortex opposite the implant.
The plate is placed on the tension side of the eccentrically loaded bone
The load is applied so that the convex tension side normally leads to distraction in the fracture zone.
The plate prevents this by compression on the concave side.
An intact medial cortex is required to convert tension into compression.

## Slide 37: USE OF LCP PLATE: INDICATIONS
Osteoporosis
Short metaphyseal/articular segment
Periprosthetic fractures
Minimally invasive plating:MIPO
Plate bridging can be done with standard plates
Conventional bridge plating
Locked bridge plating

## Slide 39: USE OF LCP PLATES
Indications:
Osteoporotic bone
Metaphyseal fractures with short articular block
"Bridging" concept

## Slide 40: THE HISTORY OF IM NAILING
1890: Gluck first description of a blocked intramedullary nail
1914-1918: Hey Groves - use of metal pins in war injuries
1937: Rush Brothers - Steinman pins for fractures of the ulna and femur
1939: "V" nail stability of fixation based on frictional forces between bone and nail.
1944: Westerborn V-nail in Scandinavia.
1946: Soeur - U-nail on leg of femur, tibia and humerus.
1947: Hansen-Street "diamond shape nail"
In the late 1940s, Küntscher designed the cloverleaf nail
1968: "Detensor" transfixation nail (Küntscher)

## Slide 41: today
Introduction of new titanium nails
Cephalomedullary devices such as PFN, PFNA, Gamma nail.
The slotted cloverleaf design was replaced by a non-slotted design that provided greater torsional stiffness
Expert IM nails (proximal humerus, proximal / distal femur, tibia)
ASLS - stable locking angle system
Notes: Nowadays, in addition to wedges made of surgical steel, titanium wedges are increasingly used, as well as new cephalomedullary wedges such as PFN, PFNA and Gamma wedge.
Studs with a notch were replaced by studs without a notch, which increased the torsional rigidity of the stud.
By expanding the indication areas to the proximal and distal segments of the long bones, expert wedges were designed
Dithe locking screws with a stable angle of fixation are zinc plated

## Slide 42
42

## Slide 43: Advantages of IM NAILS
Intramedullary nails are biologically friendly
Minimally invasive
There is no direct exposure to the fracture
Indirect reduction
Soft tissue protection
Preservation of blood supply
Shortened operation time
Load sharing device
Bone consolidation by callus formation
Notes: Intramedullaryabout wedgingis biologically friendlyabout
Minimally invasive No direct exposure to breakage Device Forsharingworkload
Indirectand repositioning Soft tissue for protection Preservation of blood supply Costanaconsolidation of callus formation
43

## Slide 44: Disadvantages of intramedullary nailing
Impossible to perform the reduction directly
Limited use in distal and proximal fractures
Reports of shoulder, knee and hip pain at the entrance portal
Endosteal vascularization damage
Risk of ARDS, fat emboli in patients with pulmonary contusion
The possibility of infection spreading along the medullary canal
Advanced instrumentation, traction table, X-ray machine-C arch is required
You need a learning curve
Exposure to X-rays

## Slide 45: Intramedullary NAILING
It is often used in the treatment of fractures of long bones (femur, tibia, humerus).
"Internal Splint"
The aim is to establish:
The length
The shaft
Rotation
Achieves:
Relative stability
II healing with callus formation

## Slide 46: Intramedullary NAILING
Less likely to break the implant than the plate
Acts as a "load sharing" implant instead of wearing it
Allows axial fracture loading after nailing.
Rotational and axial stability ensured by transfixation screws
Fracture reduction is difficult in segmental fractures
Maintaining fracture reduction in close proximity to the metaphyseal spread can be difficult

## Slide 47: Complications related to Internal Fixation
Infection
Wound dehiscence
Non-healing
Implant fracture
Fat embolism
DVT

## Slide 48
A narrow, weak plate that is too short
Insufficient number of cortical engagements
Empty space at the fracture site
Indispensable result = PA and fracture
FAILURE IN APPLICATION OF CONCEPTS
Notes: Figure from: Schatzker J, Tile M: ​​The Rationale of Operative Fracture Care. Springer-Verlag, New York, p. 320, 1987.

## Slide 49: FAILURE IN THE APPLICATION OF CONCEPTS

## Slide 50: External Fixation
Primary: Interim ("DCO")
Secondary: definitive treatment.
Advantages:
Fast application
Soft tissue issues

## Slide 51: External Fixation
The bone is transfixed above and below the fracture with pins or tensioned wires
They allow adjustment of length and axis of the bone after application.
Acquaintance of "safe corridors"
Prevent the thermal bone necrosis.
Fracture is reduced by connecting different groups of pins or wires to rods or frames.

## Slide 52: Advantages of external fixation
Minimal damage to vascularization
Minimal soft tissue damage
Fixation is distant from the site of injury
A good option when there is a significant risk of infection

## Slide 53: DISADVANTAGES of external fixation
Limited joint function
Infection around the pin
Bulky (heavy to carry)
Inadequate stability for certain fractures

## Slide 54: Indications
They are most often used in:
Tibia
Distal radius
Less commonly used:
Femur
Humerus
Forearm
Open fractures
Closed fractures with compromise of soft tissues
Periarticular fractures
Polytrauma /damage control
Pelvic fractures
Children's fractures

## Slide 55: Open fractures
Variability in severity: I - IIIC
Surgical "urgency": 6-8 hours
Time for antibiotics and debridement is crucial
Choice of antibiotics?
Cephalosporins I gen. (Cefazolin 1g/8h)
Clindamycin (600mg/12h) + Probiotic
Aminoglycosides (Amikacin 1g/24h)
Metronidazole (500mg/8h)

## Slide 56: Open fractures
Avoids the site of injury
Avoids additional injuries to soft tissues and vascularization

## Slide 57: Closed fractures with compromise of soft tissues
Swelling
Fracture bullous changes

## Slide 58: Closed fractures with compromise of soft tissues
Crash injuries
Burns

## Slide 59: Compartment Sy
Emergency surgical intervention
Result of traumatic soft tissue injury +/- fracture
Increased pressure in a closed space reduces blood flow in tissues
5 P-s: pain/pressure/paresthesia/pallor/pulsless
Location:
Lower leg
Upper leg
Foot
Buttock
Forearm
Hand

## Slide 60: Periarticular fractures
Severe fractures with involvement of the joint and expansion of the diaphysis

## Slide 61: Periarticular fractures
Bridging SF if it is axially unstable

## Slide 62: Periarticular fractures
External fixation can be combined with internal fixation=HYBRID FIXATION

## Slide 63: Polytrauma
Temporary stabilization of long bone fractures in a HD unstable patient
Minimally invasive
Reduces bleeding
Pain control
Patient care
"Damage control"

## Slide 64: PELVIC FRACTURES
Temporary stabilization for closed fractures
Bleeding control
It reduces the movement of the clot

## Slide 65: Fractures in children
Fractures of the femur
One of the alternatives of several weeks of skeletal traction
It is used less often due to the use of flexible pins

## Slide 66: external fixation
    The construction of the fixator will depend on the treatment strategy:
    Urgent - DCO
    Temporary treatment (operations in 2 acts)
    Definitive treatment

## Slide 67: construction of external fixators
External fasteners with studs
Uni-planar
Bi-planar
Multi-planar
External fixators with rings
Hybrid external fixators

## Slide 68
Uni-planar
Bi-planar
Multi-planar

## Slide 69: bridging Ex FIX
Built as uni- and multi-planar structures
Areas prone to soft tissue problems
Knee
Ankle joint
Open fractures
When multiple injuries prevent definitive treatment
Notes: Animation.
1stclick.Title and graphic
Bullets come separately.

## Slide 70: complications
Neuro-vascular injuries
Fracture and loosening of the pin
Infection around the pin
Joint Contracture
Malalignment
Compartment sy
Healing in a bad position
Non-union

## Slide 71: CONCLUSION
"… bone is a plant rooted in soft tissue, and when its vascular connections are damaged, it often requires not cabinet-making techniques, but the care and understanding of the gardener."
Respect the soft tissues!
Select the appropriate fixation method
Achieve length, axis and rotation control to enable movement as quickly as possible
Understand the requirements and limitations of each method of internal fixation

## Slide 72
Thank you for your attention